## Slide 1
PREDICTIVE MAINTENANCE
Calling trucks in before the
component fails
A cost-optimal failure-risk model on the SCANIA Component X fleet, and what it would take to run it.
Executive summary
33,000 trucks | IDA 2024 challenge cost matrix | Three-seed result

## Slide 2
THE QUESTION
What the model is actually asked
SCANIA Component X | 02
For one truck, right now: how close is the monitored component to failure, using only the readouts that truck has already sent home.
The output is an action, not a score: call this truck into the workshop, or leave it running.
Five degradation classes: class 0 is more than 48 time steps from failure, class 4 is 0 to 6 steps away.
Only 2.7% of the fleet is at risk in any scoring window. The rest are healthy and must not be disturbed.

## Slide 3
WHY ACCURACY FAILS
The economics decide the model, not the metric
SCANIA Component X | 03
500
Cost of missing a truck that fails
10
Cost of a workshop check that finds nothing
50 : 1
False alarms one real catch pays for
A model scored on accuracy predicts healthy for everyone, is right 97% of the time, and saves nothing.
We minimise expected cost instead. The model emits probabilities; the decision rule picks the cheapest action under the published cost matrix.
Low precision is correct here, not broken. Optimising precision on this loss destroys value.

## Slide 4
RESULT
Cost against every alternative policy
SCANIA Component X | 04
35,469 ± 849
Test cost, mean of three seeds
29%
Cheaper than checking every truck
0.77
Share of at-risk trucks caught
Policy | Test cost
AutoGluon LightGBM, cost-optimal rule (3 seeds) | 35,469 ± 849
Check every truck | 49,671
Act on the most likely class | 56,100
Check nothing | 56,100

## Slide 5
IN OPERATIONAL TERMS
What the number buys the workshop
SCANIA Component X | 05
109 of 142 at-risk trucks are caught before the component fails, at the tuned operating point.
About 2,100 of 5,045 trucks are called in. Checking all 5,045 catches every failure and costs 40% more.
The saving comes from not inspecting the other 2,900, while still reaching most of the trucks that were going to fail.
33 at-risk trucks are still missed. That residual is the honest cost of the current model, and it is where further work pays.

## Slide 6
BENCHMARK
Against the published results on this dataset
SCANIA Component X | 06
Approach | Test cost
Our work, AutoGluon LightGBM (3 seeds) | 35,469 ± 849
CatBoost, same study, best row read off the test set | 36,724
XGBoost, empirical study, the model they actually selected | 37,733
XGBoost, Carpentier et al., level with checking every truck | 49,671
The target is 37,733, the model the leading study selected on validation. We are 2,264 ahead of it, wider than our own seed spread of 849.
That study used AutoGluon too, so the gap comes from how the training rows and the decision rule are built, not from the toolkit.
Two deep-learning entries exist on this benchmark and both score worse, but none of the published work states its decision rule, so they are left out rather than compared on an unknown basis.

## Slide 7
CONFIDENCE
Why this number is reportable
SCANIA Component X | 07
Three seeds, not one. A single run on this data moves by more than most of the improvements teams chase on it.
The noise floor was measured, not assumed. Single-split tuning had a seed-to-seed spread of 1,668. Pooling validation into training and tuning on out-of-fold predictions halved it to 849.
A leakage audit was run and it found something. A backward fill let a scoring point read readouts from its own future. Removing it moved the result from a flattering 35,925 to an honest 39,379, before the protocol work earned the gain back.
The test set was scored once, at the end, after every decision was fixed on training data.

## Slide 8
LIMITATION
Ranking is the binding constraint
SCANIA Component X | 08
15 / 142
At-risk trucks inside the top 100 by risk
47 / 142
Inside the top 500
2,100
Alarms the cost rule actually raises
The cost win comes from alarming broadly, not from sharp ranking.
If the workshop can only take 100 trucks a day, this model finds roughly one in ten of the failures, not eight in ten.
Capacity-constrained rollout needs better ordering, which is the next piece of modelling work, not more threshold tuning.

## Slide 9
RUNNING IT FOR REAL
The loop this would sit inside
SCANIA Component X | 09
Batch scoring, not a real-time alarm. These are aggregate counters uploaded per cycle, not a live sensor stream. Trucks are rescored when new readouts arrive.
Output is a ranked work list for the planner, trimmed to what the workshop can absorb that day.
Every dispatched truck returns a label. Found or not found feeds the next training round; without that loop the model stops improving on day one.
Drift has to be watched. New vehicle configurations and new routes shift the inputs; retraining is scheduled, not incidental.
Each alert needs a reason a mechanic will accept, such as the counter that accelerated threefold over three cycles.

## Slide 10
METHOD, IN ONE SLIDE
What kind of model this is
SCANIA Component X | 10
Discrete-time survival classification on panel data. Not a sequence forecaster: the history up to a scoring point is compressed into features, and a gradient-boosted tree predicts the degradation class.
Features are rates, not levels. The counters are cumulative and never reset, so wear speed over 3, 10 and 20 readout windows carries the signal, plus acceleration, histogram drift and reporting gaps.
89% of outcomes are censored. Most trucks never failed inside the observation window, which is why a survival framing beats a plain binary classifier.
Folds are grouped by vehicle, so near-duplicate scoring points from one truck can never sit on both sides of a split.

## Slide 11
GO DEEPER
The analysis behind these numbers
SCANIA Component X | 11
Open the full EDA notebook
https://nbviewer.org/github/jiramethtmt/predictive-maintenance-time-series/blob/main/notebooks/01_eda_scania_component_x.ipynb
Repository, code and reproduction steps
https://github.com/jiramethtmt/predictive-maintenance-time-series
SCANIA Component X dataset, CC BY 4.0
https://doi.org/10.5878/jvb5-d390
Notebook source on GitHub
https://github.com/jiramethtmt/predictive-maintenance-time-series/blob/main/notebooks/01_eda_scania_component_x.ipynb